## Slide 1: Side-channel power attack against a cryptographic software
Metehan Koç
Renaud Pacalet

## Slide 2: Project Overview
Objective: Capture power traces of ASCON algorithm to extract private key by side channel attacks.
Target Hardware: 32-bit ARM chip via CW-Husky.

## Slide 3: What is ascon?
Purpose: Provides high security with low overhead, making it ideal for the Internet of Things (IoT), embedded sensors, and medical devices.
Functionality: It is primarily an Authenticated Encryption with Associated Data (AEAD) scheme, meaning it provides both confidentiality (encryption) and integrity (tamper protection) in a single process.
Design Philosophy: It is based on a sponge construction, similar to the SHA-3 (Keccak) hashing standard.

## Slide 4: Phases of ascon
Initialization: Mixes Key, Nonce, and IV into the 320-bit state.
Associated Data: Absorbs non-encrypted data into the state.
Processing: XORs plaintext/ciphertext to encrypt or decrypt.
Finalization: Generates the 128-bit tag for verification.

## Slide 5: Ascon Permutations
Addition of Round Constants: XORs a unique 1-byte constant into the middle word (S2).
Nonlinear Substitution Layer: Applies a 5-bit S-box "vertically" across all 5 words (64 times in parallel).
Linear Diffusion Layer: XORs each 64-bit word with two of its own rotated copies.
Ascon’s S-box
Ascon’s linear layer

## Slide 6: ASCON State Loading
S0: 64-bit IV (contains algorithm-specific constants).
S1, S2: 128-bit Secret Key (K).
S3, S4: 128-bit Nonce (N).

## Slide 7: Substitution layer
Assembly presentation of C code

## Slide 8: Implementation and KAT verification
Implementation: ASCON AEAD encryption and decryption algorithms implemented by using C (ascon.c, ascon.h).
Test Dataset: Utilized a comprehensive suite of 1,000 test cases derived from the official reference implementation.
Software Validation: Developed a C script (test_ascon.c) to verify encryption/decryption consistency across the entire dataset.
Result: ASCON implementation pass the all tests and it verified the correctness of the implementations.

## Slide 9: FIRMWARE
Target firmware is implemented in C.
Removed get_AD and get_PT to optimize firmware for collecting traces.
get_key: Sets the private key for ASCON.
get_nonce: Sets the nonce and starts the first permutation round.

## Slide 10: Side channel attack to ASCON
To handle the complexity of the 32-bit K0_low register, the attack uses a Divide-and-Conquer strategy combined with an iterative power model.
Target: K0_low (Lower 32 bits of the first 64-bit key chunk).
Strategy: Two 16-bit sub-key guesses (65,536 hypotheses each) to reduce computational overhead.
Power Model: Hamming Weight (HW) of the intermediate state R8, modeled as:
Dataset: 500,000 power traces processed using vectorized NumPy operations for high-speed correlation calculation.

## Slide 11: Synchronization of traces
Before running a full-scale attack on an unknown key, we use a Known Key to verify that the power traces are correctly synchronized with the ASCON cryptographic operations.
Hypothesis: If our model (R8 register state) is correct and the traces are aligned, we should see a distinct correlation spike at the exact moment that register is manipulated in hardware.

## Slide 12: Execution pipeline
Trace Centering: Pre-calculates mean traces and standard deviation to optimize the Pearson correlation loop.
Iterative Recovery:
  Phase 1: Attacks Bytes 0-1 to find the first 16 bits.
  Phase 2: Attacks Bytes 2-3 while maintaining the state of the previously recovered bits.
Statistical Selection: The candidate with the highest absolute Pearson correlation coefficient is selected as the winner for each segment.

## Slide 13: Results for ko_low
K0 recovered successfully (0x16157e2b)
Top results are all close to the actual key

## Slide 14: Results for k0_High
Results for all the bytes are wrong.
Correct bytes are not in top 10 guesses.
Possible reasons are false implementation, initial value of the register, noises.

## Slide 15: summary
1. Implementation & Environment
  Target: Successful implementation of Ascon authenticated encryption on firmware.
  Data Acquisition: Power traces collected from the target hardware.
2. Testing & Synchronization
  Testing: Ascon implementation tested both on local and target
  Trace Alignment: Verified synchronization by comparing trace graphs across different cryptographic keys
3. Side-Channel Attack (SCA)
  Side channel attack is performed by using Pearson Correlation
  K0_low: Successfully recovered with high confidence
  K0_high: Currently not recovered; further noise reduction or trace amplification required.

## Slide 16: references
https://ascon.isec.tugraz.at/index.html
https://github.com/newaetech/chipwhisperer
https://chipwhisperer.readthedocs.io/en/latest/index.html
https://github.com/ascon/ascon-c/

## Slide 17
Thank you for listening